## Slide 1: Development of a lunar orbit propagator
Study of low lunar frozen orbits, DROs and NRHOs in the vicinity of the moon
Quentin Granier
Research Associate
Eyes on the Solar System - Moon - NASA/JPL
Eyes on the Solar System - Moon - NASA/JPL

## Slide 2
  The basics of DROs and NRHOs
DRO and NRHO: family of 3 body problem orbits in the rotational plane
Calculated in the simplified model: CR3BP (Circular Restricted 3 Body Problem)
Build in the rotational plane
DRO
NRHO
Inertial frame
Rotational frame
Mission example
Orion (Artemis I)
Capstone (Gateway)

## Slide 3: Plan
  Improvement of an existing propagator
    Assessment of the propagator
    Improvement of the model
  Use of the propagator to study and generate interesting orbits
    DROs
    NRHOs

## Slide 4
Improvement of an existing propagator
Existing propagator with 1 force 6 perturbations
Perturbations taken into account:
  Gravitational field of the moon and solid tide
  Point mass attraction of the earth and sun
  General relativity correction
  Sun radiation pressure
  Earth albedo
Assessment:
  We take as an initial situation the state of the LRO spacecraft on the 1st Feb 2020
  We propagate 1 day and compare every 30 sec with the true position
Bend spacetime that needs general relativity correction
Solar radiation pressure on a satellite

## Slide 5
Improvement of an existing propagator
Improvement
Perturbations taken into account:
  Improvement lunar gravitational field  newest data (GRAIL)
    165  350 stable harmonics: Great improvement
  Improvement earth gravity field instead of point mass
    Little improvement
  General relativistic correction formula
    Error in the given formula
  Integrators choice: High order Runge Kutta and multistep integrator (Shampine Gordon)
    Best is ode45, Runge Kutta of 5th order for stability and accuracy
    Decrease the relative tolerance from 1e-6 to 1e-7
  Point mass of Jupiter
    Little improvement
GRAIL A and B on mission

## Slide 6
Improvement of an existing propagator
Before any improvement, 1 day propagation
After improvement, 4 days propagation

## Slide 7
  Use of the propagator to study and generate interesting orbits
Goal: Generate a chosen DRO or NRHO in ephemeris for some given time
=
Find an initial value that propagates into a real DRO/NRHO
DRO
NRHO
Inertial frame
Rotational frame
Mission example
Orion (Artemis I)
Capstone (Gateway)

## Slide 8
  Use of the propagator to study and generate interesting orbits
DROs:
  We know how to generate a DRO in the CR3BP
  Transition from CR3BP in Rotational to true Inertial plane, suppositions:
    Moon on same place
    Earth direction same  arbitrary choices that give
    CR3BP Earth is at average distance from moon good results
Propagate a fitted initial position
Converging to a real DRO by modifying the initial velocity
4 months propagation of such a DRO:
Very stable

## Slide 9
  Use of the propagator to study and generate interesting orbits
NRHOs:
  Same fitting
  Do not converge easily by changing one initial component (Vθ for the DROs)
  A lot less stable
Future of the project:
  Build an optimization algorithm to converge to a better initial state (start with gradient descent)
  Create a building method with small periodic maneuvers to generate several year stable NRHOs
  Same for DRO even without maneuvers
20 days propagation: Not enough stable

## Slide 10
  Thanks !
The Moon, the earth and all satellites around them
L2 Southern Halo Orbit (with Capstone NRHO)